## Slide 1: Infineon PSOC6 Lecture project status
Team: Radar Box Item Classification
Team Members: Moritz Mader, Harald Fuchs, Manuel Hackl
Achieved since the last meeting :
Formed team of 3
defined use case: "Radar-based container presence detection
recorded initial datasets for static object detection
Developed and compared 1D-Convolution and 2D-Convolution architectures
1D-CNN prototype operational detects empty box in fixed setup with high positional sensitivity
Activities planned until next meeting:
Collect data in varied environments to reduce background bias
Train for positional variance (move box slightly during recording) to fix "exact position" dependency.
Validate model performance under changing environmental conditions
Issues / Support needed:
Current model overfits to the specific lab setup/background
Model fails if the box is shifted slightly, need strategies for spatial invariance
Best practices for training a model that works across different locations (Home vs. Lab)?
1. Progress report

## Slide 2: Infineon PSOC6 Lecture project status
Achieved since last meeting:
Collected additional data to increase model’s prediction confidence
Introduced intentional variations in the physical placement of the box during data measurements
Performed data capture sessions with metal objects inside the box
Activities planned until next meeting:
Conduct further measurements with metal objects inside the box
Optimize the training process to achieve a better performing model
Issues / Support needed:
Identified significant variance in raw data between different radar boards
Deploying a model on a different board leads to a higher rate of false predictions.
2. Progress report

## Slide 3: Infineon PSOC6 Lecture project status
Achieved since last meeting:
Expanded the dataset to increase the model’s training base
Introduced intentional environmental variations
Increased data volume did not lead to improvement
the model only “works” in the lab
Activities planned until next meeting
Transforming the trained model into c code for hardware implementation
Finalizing a local http server to visualize real time data
Issues / Support needed
Models do not improve
3. Progress report

## Slide 4: Infineon PSOC6 Lecture presentation and final submission plans
Short project presentation:
Any special equipment need for demo at the demo Day ?